## Slide 1: A Python plug-in for Data logging analysis for intrusion detection system
Presented BY jayasree Boya
ShivaJyothi Angala
Notes: Industrial control system intrusion detection is a popular topic of research for several years, and many intrusion detection systems (IDS) have been proposed in literature. IDS researchers lack a common framework to train and test proposed algorithms. This leads to an inability to properly compare proposed IDS and limits research progress.

## Slide 2: Introduction
SCADA AND LOG ANALYSIS
We are using Gas Pipeline dataset for data log analysis for detecting the attacks to scale it into intrusion detection system.
There aren’t many IDS systems for detecting attacks on the virtual gas systems or any other similar systems
Our contribution is to protect those systems from several attack types. For Eg: Setpoint Attack, Pump Attack, System Mode Attack, Bad CRC Attack, etc..,
Notes: Supervisory control and data acquisition (SCADA) systems should establish logging standards and procedures to ensure that adequate information is collected by logs and security software and that the data is reviewed regularly. The length of time to maintain log data is dependent on several factors, including the organization’s data retention policies and the volume of data. As each business has different needs and regulatory requirements, legal counsel should be obtained to determine the appropriate retention schedule for logs.
Changes the pressure set point outside and inside of the range of normal operation.
Sends MODBUS packets with incorrect CRC values. This can cause denial of service.
.

## Slide 3: SCADA
Supervisory control and data acquisition (SCADA) is a control system architecture that uses computers, networked data communications and graphical user interfaces for high-level process supervisory management
It uses other peripheral devices such as programmable logic controllers and discrete PID controllers to interface to the process plant or machinery.
Notes: are highly distributed systems used to control
geographically dispersed assets
v Provides centralized data acquisition, monitoring,
and control in real time

## Slide 4: Intrusion detection system
Intrusion detection is the process of monitoring the events occurring in a computer system or network and analyzing them for signs of possible incidents, which are violations or imminent threats of violation of computer security policies, acceptable use policies, or standard security practices.
An intrusion detection system (IDS) is software that automates the intrusion detection process.
Security Log Analysis Systems are also known as Log-based Intrusion Detection Systems (LIDS). Log Analysis for Intrusion Detection is the process or techniques used to detect attacks on a specific environment using logs as the primary source of information

## Slide 5: modbus
Modbus RTU is an open, serial (RS-232 or RS-485) protocol derived from the Master/Slave architecture. It is a widely accepted protocol due to its ease of use and reliability.
Modbus RTU is widely used within Building Management Systems (BMS) and Industrial Automation Systems (IAS).
The MODBUS protocol defines a simple Protocol Data Unit (PDU) independent of the underlying communication layers. The mapping of MODBUS protocol on specific buses or networks can introduce some additional fields on the Application Data Unit (ADU).
The client that initiates a MODBUS transaction builds the MODBUS Application Data Unit. The function code indicates to the server which kind of action to perform.

## Slide 6: Related work
Industrial Control System Simulation and Data Logging for Intrusion Detection System Research
Notes: . This paper documents 2 approaches to data sharing for the industrial control system IDS research community. First, a network traffic data log captured from a gas pipeline is presented. The gas pipeline data log was captured in a laboratory and includes artifacts of normal operation and cyberattacks. Second, an expandable virtual gas pipeline is presented which includes a human machine interface, programmable logic controller, Modbus/TCP communication, and a Simulink based gas pipeline model. The virtual gas pipeline provides the ability to model cyber-attacks and normal behavior. IDS solutions can overlay the virtual gas pipeline for training and testing.

## Slide 7: Approach
Split the fields from the data and structure it into an object
Check for the “specific result” filed of the object.
If the value of “specific result” is between (1-35) identify that as an attack and process the object and get the Attack Name, Address and other information.
Collect the number of attacks and its type

## Slide 8: Execution

## Slide 9: Challenges and limitations
Structuring data into the objects because some fields doesn’t have valid data.
Unable to adapt into changing environment because this is created for virtual gas pipeline system.

## Slide 10: conclusion:
Scale the project into intrusion detection system
The data logs include artifacts of 35 cyber attacks and can be used to train and test classifiers used by IDS
The attacks are tabulated into 5 categories: NMRI, CMRI, MSCI, MPCI

## Slide 11: Questions
Thank you 